## Slide 1
Demonstration
A Python-based user interface:
Waveform and spectrogram views are supported.
User-configurable montages and filtering.
Scrolling by time or by next event.
Channel-dependent scaling.
Events can be viewed per channel, per epoch, or selectively filtered.
The TUH EEG Data Corpus
The corpus development involved the pairing, de-identification and annotation of EEG data:
EEG reports were manually verified and de-identified.
The TUH EEG Data Corpus
Automatic Interpretation of EEGs for Clinical Decision Support
Abstract
  Introduction: Manual review of an EEG by a neurologist is time-consuming and tedious. Interrater agreement is low for annotation of low-level events such as spikes and sharp waves. We present a high performance classification system based on big data and machine learning.
  Methods: Uses a combination of hidden Markov models (HMMs) for sequential decoding and deep learning for postprocessing. The system detects three events of clinical interest: (1) spike and/or sharp waves, (2) periodic lateralized epileptiform discharges, and (3) generalized periodic epileptiform discharges. The system also detects three events used to model background noise: (1) artifacts, (2) eye movement and (3) background.
  Results: Target for clinical performance was a detection rate of 95% with a false alarm rate below 5%. Our system produced a detection rate of 89% while maintaining a false alarm rate of 4%. The postprocessing also improved accuracy on spike detection from 25% to 55%.
  Conclusion: The TUH EEG Corpus provides a sufficient amount of data to apply powerful machine learning algorithms. Performance is now approaching that required for clinical acceptance.
Summary
  The TUH EEG Corpus represents a unique opportunity to advance EEG analysis using state of the art machine learning.
  The 2002–2014 data is publicly available. See www.nedcdata.org for more details.
  Baseline performance of a multi-pass hybrid HMM/deep learning classification system is promising: 89% DET / 4% FA.
  AutoEEG runs hyper real-time on a standard PC processor.
  Future Work
  The TUH EEG Corpus will continue to grow at a rate of 3,000 EEGs per year, and will expand to multiple collection sites (pending funding).
  Improved active learning will enable training of better models.
  Enhanced feature extraction, discriminative decoding and adaptation will improve performance.
  Real-time detection of seizures for ICU applications is our next focus.
  Cohort retrieval will be integrated into our Python-based demonstration.
Acknowledgements
Research reported in this poster was supported by National Human Genome Research Institute of the National Institutes of Health under award number 1U01HG008468.
The content is solely the responsibility of the authors and does not necessarily represent the official views of the National Institutes of Health.
The TUH EEG Corpus development was sponsored by the Defense Advanced Research Projects Agency (DARPA), Temple University’s College of Engineering and Office of the Vice Provost for Research.
Classification Performance
6-way confusion matrix after HMM pass (P1):
Confusion matrix after post-processing (P2+P3):
Detection error tradeoff (DET) curve (P1):
Delta features become more significant when the detection rate is high.
False alarm rate rises rapidly at detection rates above 70%.
Post-processing improves detection rate while maintaining a low false alarm rate:
Copy EEG files to Disks
Convert EEG files to EDF
Capture Physicians' Reports
Deidentify Reports
Label Generation
Hard Copies
Alpha Database
M*Modal Database
Optical Character Recognition
Copy EEG files to Disks
Access Database
 | SPSW | PLED | GPED | EYBL | ARTF | BCKG
SPSW | 40% | 5% | 33% | 10% | 8% | 4%
PLED | 20% | 55% | 18% | 4% | 1% | 2%
GPED | 12% | 22% | 51% | 2% | 7% | 6%
EYBL | 3% | 9% | 2% | 84% | 1% | 1%
ARTF | 6% | 3% | 4% | 2% | 39% | 46%
BCKG | 9% | 2% | 8% | 3% | 6% | 72%
 | SPSW | PLED | GPED | EYBL | ARTF | BCKG
SPSW | 41% | 0% | 33% | 3% | 5% | 18%
PLED | 14% | 39% | 30% | 0% | 3% | 14%
GPED | 1% | 9% | 87% | 1% | 0% | 2%
EYBL | 0% | 0% | 0% | 69% | 2% | 29%
ARTF | 5% | 0% | 2% | 13% | 10% | 70%
BCKG | 3% | 0% | 1% | 7% | 1% | 88%
References
Lopez, S., et al. (2015). Automated Identification of Abnormal EEGs. Proceedings of the EEE Signal Processing in Medicine and Biology Symposium (pp. 1–4). Philadelphia, Pennsylvania, USA.
Harati, A., et al. (2015). Improved EEG Event Classification Using Differential Energy. Proceedings of the IEEE Signal Processing in Medicine and Biology Symposium (pp. 1–4). Philadelphia, Pennsylvania, USA.
Harati, A., et al. (2014). THE TUH EEG CORPUS: A Big Data Resource for Automated EEG Interpretation. Proceedings of the IEEE SPMB Symposium (pp. 1-5). Philadelphia, PA, USA.
System | Detection Rate | False Alarm | Error
Heuristics | 99% | 64% | 74%
Random Forest | 85% | 6% | 37%
HMM (P1) | 84% | 4% | 37%
+ Deep Learning (P1+P2) | 82% | 4% | 39%
+ Language Model (P1+P2+P3) | 89% | 4% | 36%
A. Harati
Jibo, Inc.
Redwood City, California, USA
M. Golmohamaddi, S. Lopez I. Obeid and J. Picone
The Neural Engineering Data Consortium
Temple University, Philadelphia, Pennsylvania, USA
M. Jacobson
The Temple University Katz School of Medicine
Temple University, Philadelphia, Pennsylvania, USA
S. Tobochnik
New York-Presbyterian Hospital / Columbia University Medical Center, New York City, New York, USA
Introduction
Modern machine learning algorithms require big data to accurately train complex statistical models.
The TUH EEG Data Corpus is the largest publicly available database of clinical EEGs, and is enabling the development of high performance automatic interpretation systems.
AutoEEG is a hybrid system based on hidden Markov models and deep learning:
Events of Interest
Six events of interest based on multiple iterations with board certified neurologists:
Collapse background classes to one class for scoring (4-way).
Collapse to two classes (Epileptiform and Background) for DET curve scoring and analysis.
TUH EEG CORPUS
Feature Extraction
Sequential Modeler
Post Processor
Epoch
Label
Epoch
Temporal and Spatial Context
Hidden Markov Models
Finite State Machine
Epileptiform | Background
SPSW: Spike and sharp wave | ARTF: Artifact
GPED: Generalized periodic epileptiform discharges and triphasic | EYBM: Eye Movement
PLED: Periodic lateralized epileptiform discharges | BCKG: Background
Feature Extraction
Standard frequency domain analysis is used based on cepstral features and deltas (P1):
No. | System Description | Dims | 6-Way | 4-Way | 2-Way
1 | Cepstral | 7 | 59.3% | 33.6% | 24.6%
2 | Cepstral + Ef | 8 | 45.9% | 33.0% | 24.0%
5 | Cepstral + Ef +Ed | 9 | 39.2% | 30.0% | 20.4%
6 | Cepstral +  | 14 | 56.6% | 32.6% | 23.8%
7 | Cepstral + Ef +  | 16 | 43.7% | 30.1% | 21.2%
8 | Cepstral + Et +  | 16 | 42.8% | 31.6% | 22.4%
9 | Cepstral + Ed +  | 16 | 51.6% | 30.4% | 22.0%
10 | Cepstral + Ef +Ed +  | 18 | 35.4% | 25.8% | 16.8%
11 | Cepstral +  +  | 21 | 53.1% | 30.4% | 21.8%
12 | Cepstral + Ef +  +  | 24 | 39.6% | 27.4% | 19.2%
13 | Cepstral + Et +  +  | 24 | 39.8% | 29.6% | 21.1%
14 | Cepstral + Ed +  +  | 24 | 52.5% | 30.1% | 22.6%
15 | Cepstral + Ef +Ed +  +  | 27 | 35.5% | 25.9% | 17.2%
16 | (15) but no  for Ed | 26 | 35.0% | 25.0% | 16.6%
Active Learning Approach to Training
EEG reports only contain summaries; a small amount of manually-labeled data available.
Seed models based on manually-annotated data.
Train, classify, and select high-confidence data.
Iterate:
Feature Extraction
Find best alignment between primitives and data
Alignment Found?
Recall Parameters
Supervised learning process
Reestimate Parameters
TUH EEG Corpus
Input: EEG Raw Data
Output: Model Parameters