## Slide 1
Automated Identification of
Abnormal Adult EEG
S. López, G. Suarez, D. Jungreis, I. Obeid and J. Picone
Neural Engineering Data Consortium
Temple University

## Slide 2
  Interpretation of EEG is done by trained and certified physicians.
  The interpretation of an EEG depends on the subjective judgement of the examiner.
  Increasing the interrater agreement for EEG interpretation plays a key role in the assessment of the validity for this technique.
Manual Interpretation of EEGs
Patient Preparation
EEG Recording
EEG ranging from 22 minutes to several days is recorded
EEG is Interpreted
Certified physicians interpret EEG
Patients are prepared for the test
EEG Report is Produced
Report of findings and normality or Abnormality of the record is prepared

## Slide 3: Normal/Abnormal Classification
  When reports are generated, the records are categorized as either normal or abnormal.
  Automatic classification of EEGs as normal or abnormal is a significant step for the reduction of the visual bias.
  The normal/abnormal decision is made through the examination of the presence of abnormal EEG events or lack of normal EEG characteristics.
Normal EEG
Abnormal EEG
Possible benign variables
Presence of normal EEG characteristics
Presence of abnormalities
Lack of normal EEG characteristics

## Slide 4: Normal EEG Characteristics
  The main characteristics of a normal EEG are the following:
    Reactivity: Response to certain physiological changes or provocations.
    Alpha Rhythm: Waves originated in the occipital lobe (predominantly), between 8-13 Hz and 15 to 45 μV.
    Mu Rhythm: Central rhythm of alpha activity commonly between 8-10 Hz visible in 17% to 19% of adults.
    Beta Activity: Activities in the frequency bands of 18-25 Hz, 14-16 Hz and 35-40 Hz.
    Theta Activity: Traces of 6-7 Hz activity present in the frontal or frontocentral regions of the brain.
  The normal/Abnormal classification heavily depends on the frequency, presence or distortion of this feature. Its emergence during the closed-eyes period is known as Posterior Dominant Rhythm (PDR)
  We decided to focus on this characteristic.

## Slide 5: Data
  The data used was a subset of the TUH EEG Corpus. The data was divided as follows:
Set | Normal | Abnormal
Training | 102 EEGs | 100 EEGs
Development | 50 EEGs | 50 EEGs
Evaluation | 50 EEGs | 50 EEGs
  Because the PDR can be observed in the posterior and occipital channels, channel T5-O1 was selected for the experiments.

## Slide 6: Experimental Design
First 60 seconds of each EEG recording were used
Signal Features were extracted
MFCC-like features (8 cepstral coefficients)
Differential Energy
Vectors for the selected channel were concatenated in a supervector
First and second derivatives
PCA was used to reduce the dimensionality of the feature matrix.

## Slide 7: Algorithms
  Two standard Algorithms were explored and compared:
    k-Nearest Neighbor (kNN)
    Random Forest
  Systems for different values of k were tested
…
+
Decision

## Slide 8: Random Forest and the Number of Trees
The performance of the systems higher than 20 trees are comparable to each other.
Taking performance and computational time for the classification into account, a number of 50 trees was chosen for the rest of the experiments.

## Slide 9: Knn: Tuning the system
The lowest k for the best operating interval was chosen.
This point corresponds to k = 20.
The best error rate achieved by the system is 41.79% for k = 86.

## Slide 10: Comparing the Two Systems
For PCA dimensions higher than 20 both systems perform better than guessing based on priors (49.79% error rate).
99.82% of the variance is explained by the first principal component

## Slide 11: Channel Comparison
The performance for the T5-O1 channel was better for all operating points with PCA dimensions higher than 20.
This correlates with the information learned from physicians about their reliance on occipital channels for the classification of EEGs.

## Slide 12: Error Analysis
 | Normal | Abnormal
Normal | 50.49% | 49.50%
Abnormal | 34.00% | 66.00%
No. | System Description | Error
1 | Random Guessing | 49.75%
2 | kNN (k = 20) | 41.79%
3 | RF (Ntrees = 50) | 31.66%

## Slide 13
Normal/Abnormal Classification:
  These pilot experiments have allowed the creation of a normal/abnormal baseline system.
  The classification decisions were made through the random forest ensemble learning and later compared to the kNN algorithm and the guessing based on priors.
  Results show that kNN and random forest outperform guessing based on priors.
  Knowledge about the PDR and its characteristics was used for selecting a significant EEG channel
  Events that encapsulate benign EEG variants should be labeled and incorporated into the system
  Time should be invested in the analysis and extraction of features that are more meaningful and adequate for this particular problem.
Summary

## Slide 14
Brief Bibliography
[1] F. Fahoum, R. Lopes, F. Pittau, F. Dubeau, and J. Gotman, “Widespread epileptic networks in focal epilepsies: EEG-fMRI study,” Epilepsia, vol. 53, no. 9, pp. 1618–1627, Sep. 2012.
[2] H. Azuma, S. Hori, M. Nakanishi, S. Fujimoto, N. Ichikawa, and T. A. Furukawa, “An intervention to improve the interrater reliability of clinical EEG interpretations,” Psychiatry Clin. Neurosci., vol. 57, no. 5, pp. 485–489, Oct. 2003.
[3] S. Smith, “EEG in the diagnosis, classification, and management of patients with epilepsy,” J. Neurol. Neurosurg. Psychiatry, vol. 76, no. Suppl 2, pp. ii2–ii7, Jun. 2005.
[4] J. S. Ebersole and T. A. Pedley, Current practice of clinical electroencephalography, 4th ed. Philadelphia, Pennsylvania, USA: Wolters Kluwer, 2014.
[5] A. Harati, S. Lopez, I. Obeid, M. Jacobson, S. Tobochnik, and J. Picone, “THE TUH EEG CORPUS: A Big Data Resource for Automated EEG Interpretation,” in Proceedings of the IEEE Signal Processing in Medicine and Biology Symposium, 2014, pp. 1–5.

## Slide 15
[6] A. C. N. Society, “Guideline 6: A Proposal for Standard Montages to Be Used in Clinical EEG [White Paper]. Retrieved from http://www.acns.org/pdf/guidelines/Guideline-6.pdf, 2006.
[7] A. Harati, M. Golmohammadi, S. Lopez, I. Obeid, and J. Picone, “Improved EEG Event Classification Using Differential Energy,” in Proceedings of the IEEE Signal Processing in Medicine and Biology Symposium, 2015, pp. 1–4.
[8] I. T. Jolliffe, Principal Component Analysis, 2nd ed. New York City, New York, USA: Springer-Verlag, 2002.
[9] R. O. Duda, P. E. Hart, and D. G. Stork, Pattern classification, 2nd ed. New York City, New York, USA: John Wiley & Sons, 2003.
[10] L. Breiman, J. Friedman, R. A. Olshen, and C. Stone, Classification and Regression Trees, 1st ed. Boca Raton, Florida, USA: Chapman and Hall/CRC, 1984.
[11] Mathworks, “TreeBagger,” Statistics and Machine Learning Toolbox, 2015. [Online]. Available: http://www.mathworks.com/help/stats/ treebagger.html. [Accessed: 18-Oct-2015].
[12] A. Ganapathiraju, J. Hamaker, and J. Picone, “Applications of Support Vector Machines to Speech Recognition,” IEEE Trans. Speech Audio Process., 2002.
Brief Bibliography

## Slide 17
The Neural Engineering Data Consortium Mission: To focus the research community on a progression of research questions and to generate massive data sets used to address those questions. To broaden participation by making data available to research groups who have significant expertise but lack capacity for data generation.
Impact:
  Big data resources enables application of state of the art machine-learning algorithms
  A common evaluation paradigm ensures consistent progress towards long-term research goals
  Publicly available data and performance baselines eliminate specious claims
  Technology can leverage advances in data collection to produce more robust solutions
Expertise:
  Experimental design and instrumentation of bioengineering-related data collection
  Signal processing and noise reduction
  Preprocessing and preparation of data for distribution and research experimentation
  Automatic labeling, alignment and sorting of data
  Metadata extraction for enhancing machine learning applications for the data
  Statistical modeling, mining and automated interpretation of big data
  To learn more, visit www.nedcdata.org

## Slide 18
The Temple University Hospital EEG Corpus Synopsis: The world’s largest publicly available EEG corpus consisting of 20,000+ EEGs collected from 15,000 patients, collected over 12 years. Includes physician’s diagnoses and patient medical histories. Number of channels varies from 24 to 36. Signal data distributed in an EDF format.
Impact:
  Sufficient data to support application of state of the art machine learning algorithms
  Patient medical histories, particularly drug treatments, supports statistical analysis of correlations between signals and treatments
  Historical archive also supports investigation of EEG changes over time for a given patient
  Enables the development of real-time monitoring
Database Overview:
  21,000+ EEGs collected at Temple University Hospital from 2002 to 2013 (an ongoing process)
  Recordings vary from 24 to 36 channels of signal data sampled at 250 Hz
  Patients range in age from 18 to 90 with an average of 1.4 EEGs per patient
  Data includes a test report generated by a technician, an impedance report and a physician’s report; data from 2009 forward inlcudes ICD-9 codes
  A total of 1.8 TBytes of data
  Personal information has been redacted
  Clinical history and medication history are included
  Physician notes are captured in three fields: description, impression and correlation fields.

## Slide 19
Automated Interpretation of EEGs Goals: (1) To assist healthcare professionals in interpreting electroencephalography (EEG) tests, thereby improving the quality and efficiency of a physician’s diagnostic capabilities; (2) Provide a real-time alerting capability that addresses a critical gap in long-term monitoring technology.
Impact:
  Patients and technicians will receive immediate feedback rather than waiting days or weeks for results
  Physicians receive decision-making support that reduces their time spent interpreting EEGs
  Medical students can be trained with the system and use search tools make it easy to view patient histories and comparable conditions in other patients
  Uniform diagnostic techniques can be developed
Milestones:
  Develop an enhanced set of features based on temporal and spectral measures (1Q’2014)
  Statistical modeling of time-varying data sources in bioengineering using deep learning (2Q’2014)
  Label events at an accuracy of 95% measured on the held-out data from the TUH EEG Corpus (3Q’2014)
  Predict diagnoses with an F-score (a weighted average of precision and recall) of 0.95 (4Q’2014)
  Demonstrate a clinically-relevant system and assess the impact on physician workflow (4Q’2014)