## Slide 1: Development of a fast and efficient algorithm for p300 event related potential detection
A master’s thesis Presentation
by Elliot Franz
Advisor: Iyad Obeid, phd
ECE Department, Temple University

## Slide 2: Presentation overview
Project Background
BCI Dataset
Experimental Design
Data Processing
Phase I Results
Phase II Results
Shortcomings/Future work

## Slide 3: 1.) Background Overview
Timeline
Brain Computer Interfaces
P300 Event Related Potential (ERP)
P300 Speller
Emotiv EPOC
Grass Model 12 Neurodata Acquisition System

## Slide 4: TimeLine From Proposal

## Slide 5: Brain computer Interfaces
What are BCIs?
Why BCIs?
How is brain data acquired?
  Surface EEG, Intercranial EEG, Funtional MRI (fMRI)

## Slide 6: P300 Event Related Potential
What is P300?
Why P300 BCI?
How is
P300 elicited?
  Three protocols
  Oddball
J. Polich, Clinical Neurphysiology. 2007

## Slide 7: Factors which affect p300
A variety of biological factors affect the latency and the amplitude of the P300 ERP
  Eating food
  Body temperature
  Exercise
  Rarity of target
  Inter-stimulus Interval (ISI)

## Slide 8: P300 Speller
H. Cecotti, et al. Pattern Analysis and Machine Intelligence. 2011

## Slide 9: Emotiv EPOC
14 saline electrodes (plus 2 reference) EEG headset
Proprietary 2.4 GHz wireless
Unshielded wires
12 bit A/D converter
0.51 μV resolution
On board pre-filters
  0.2 – 45 Hz bandpass
M. Duvinage, et al. Biomedical Engineering. 2012

## Slide 10: Emotiv EPOC
Image: www.emotiv.com

## Slide 11: Grass Model 12 Neurodata acquisition system
Capable of recording from 21 Channels
Analog Filters
  Capable of bandpass filtering signals (in these experiments, analog signals were filtered between 0.1 and 300 Hz)
  Notch filter at 60 Hz

## Slide 12: Presentation overview
Project Background
BCI Dataset
Experimental Design
Data Processing
Phase I Results
Phase II Results
Shortcomings/Future work

## Slide 13: 2.) BCI Dataset Overview
Comparison of Electrode Locations
Algorithm Classification Accuracy (8 parietal electrodes)
Algorithm Classification Accuracy (1 electrode)
Computation Time
2003 BCI Competition Winners

## Slide 14: Averaged recordings over cz and CP5

## Slide 15: Classification accuracy (8 parietal electrodes)

## Slide 16: Classification Accuracy (1 Electrode)

## Slide 17: Bci Winners
A. Rakotomamonjy, et al. IEEE Transactions on Biom. Engr. 2008

## Slide 18: Computation Time

## Slide 19: Presentation overview
Project Background
BCI Dataset
Experimental Design
Data Processing
Phase I Results
Phase II Results
Shortcomings/Future work

## Slide 20: 3.) Experimental Design Overview
Block Diagram of Experiment
Hardware Preparation
  EPOC
  Grass Amplifiers
Software Preparation
  OpenViBE
  TestBench
  LabView SignalExpress
Patient Instruction and Recording Environment
Recording Details

## Slide 21: Experimental Setup

## Slide 22: Hardware Preparation
EPOC
  Moisten Saline electrodes
  Place headset backwards on head and power on
Grass Electrodes
  Using Tensive gel and medical tape, apply electrodes to scalp as closely as possible to the saline electrodes towards the top and center of the head
  Isoground and reference electrode used in addition to 8 channels
  Place cap over electrodes to secure

## Slide 23: Software preparation
OpenViBE
  Close all background programs on simulating computer
  Choose appropriate number of characters to spell
  Position spelling matrix on display for patient
TestBench
  Configure software to receive markers from COM port
LabView Signal Express
  Choose 9 channels to record from on the SCB-68 (one channel is the marker channel)
  Set collection parameters (NRSE, 240 Hz sampling rate)
Notes: In an NRSE measurement system, all measurements are still made with respect to a single-node analog input sense (AISENSE), but the potential at this node can vary with respect to the measurement system ground. The previous figure illustrates that a single-channel NRSE measurement system is the same as a single-channel differential measurement system. http://zone.ni.com/reference/en-XX/help/370466V-01/measfunds/refsingleended/

## Slide 24: Recording details
Emotiv EPOC
  Sampling rate of TestBench is 128 Hz
  2.4 GHz wireless dongle transmits signals from EPOC to recording computer
Grass Model 12 Neurodata acquisition system
  Amplification set to 20,000 times
  Bandpass filtering between 0.1 and 300 Hz
  Sampling rate is 240 Hz
  SCB-68 serves as the input for 8 channels from amplifiers and 1 channel from the COM port on the simulating computer

## Slide 25: Recording Environment
Consistent lighting and size of spelling matrix through all trials
  30.5 cm wide by 28 cm height
Patient seated eye-level from matrix one meter away
Stimulus flashed for 210 ms, matrix blank for 265 ms
20 characters spelled followed by a five minute break (room lights on) and 15 more spelled characters

## Slide 26: Patient instructions
Make note of the character to spell at the beginning of each epoch
  It appears highlighted in green prior to the start of each epoch
Sit as still as possible
Mentally count the number of times the target character flashes

## Slide 27
A subject is seated facing the screen with the 6x6 character matrix displayed. The subject is wearing a cloth cap which helps to secure the gold cup electrodes. Holes have been cut in the cap for the EPOC electrodes to contact the scalp. The overhead lighting is turned on in this picture, but is turned off during actual trials.

## Slide 28: Presentation overview
Project Background
BCI Dataset
Experimental Design
Data Processing
Phase I Results
Phase II Results
Shortcomings/Future work

## Slide 29: 4.) Data processing Overview
Preprocessing
Implementation of Spatial Filters and Classification Algorithms
Implementation of Row and Column Eliminating Algorithms

## Slide 30: Preprocessing
Data Recorded from the following parietal electrodes:

## Slide 31: Preprocessing
Data separated into 1 second epochs
Each channel bandpass filtered between 0.1 and 15 Hz with a fourth order Butterworth filter
Downsampled to 40 Hz (40 samples for a 1 second epoch)
Data scaled to the interval (-1,1)
Data averaged over n intensification cycles (where n = 1, 2, 3, 7, 15)
If used, spatial filter applied here

## Slide 32: Spatial Filters
Grand Averaging, ICA, and PCA implemented in MATLAB

## Slide 33: Classification Algorithms
P300 Detection is a binary classification problem
  Identify target or non-target
Algorithms used: FLDA, BLDA, PCM, SVM, Parallel FLDA, and Parallel BLDA
  MATLAB packages used to implement all algorithms (except PCM)

## Slide 34: Parallel methods

## Slide 35: Presentation overview
Project Background
BCI Dataset
Experimental Design
Data Processing
Phase I Results (Three Subjects)
Phase II Results (Five Subjects)
Shortcomings/Future work

## Slide 36: EPOC Results

## Slide 37: Grass Amplifier Results

## Slide 38: Row and column eliminating algorithms
Number of errors by random chance:
2 Eliminated = 22 errors
4 Eliminated = 40 errors
6 Eliminated = 54 errors

## Slide 39
Row and column eliminating algorithms

## Slide 40: Presentation overview
Project Background
BCI Dataset
Experimental Design
Data Processing
Phase I Results (Three Subjects)
Phase II Results (Five Subjects)
Shortcomings/Future work

## Slide 41: EPOC Results

## Slide 42: Grass Amplifier Results

## Slide 43
Phase I
Phase II
Grand Averaging
PCA

## Slide 44: Row and column eliminating algorithms

## Slide 45: Row and column eliminating algorithms

## Slide 46: Presentation overview
Project Background
BCI Dataset
Experimental Design
Data Processing
Phase I Results (Three Subjects)
Phase II Results (Five Subjects)
Shortcomings/Future work

## Slide 47: Future work
Test real-time row/column eliminating P300 speller
  Evaluate character accuracy
  Compare accuracies of this method vs. accuracies with 15 intensifications
  Evaluate time savings
More subjects and multiple sessions
  Pick appropriate sample size based on population, confidence interval, and confidence level

## Slide 48: Shortcomings
Oxidization of saline electrodes over time
Small number of subjects (3 subjects for Phase I and 5 subjects for Phase II)
No tracking of subject improvement over multiple sessions
Electrodes used for analysis were pre-set
  Implement recursive electrode elimination

## Slide 49: acknowledgements
Thanks to Dr. Iyad Obeid and the committee for useful project advice, Andrew Williams for assistance in collection of data, and the Electrical Engineering Department of Temple University for funding