TEST # 3 REWORK

EE3133-01

Name :  Wayne Cospelich

Date Due:  May 7, 1997

Instructor:  Dr. Joseph Picone

EE3133-01				EXAM #3			PAGE 2 OF 7

PROBLEM NO. 1:  For the following system:

For c = ½, use the Nyquist criterion to determine stability

Y(s) = .25[.5X(s) + csY(s)]

Y(s) = [1 - .25csY(s)] = .125X(s)

Substituting ½ into c the following transfer function occurs:

For this problem we are needing to use the Nyquist criterion in order to determine stability.  The Nyquist plot allows us to predict the stability and performance of a closed-loop system by observing its open-loop behavior.  The Nyquist criterion is a way of checking for right half poles.

The denominator of the transfer function must be looked at along a contour encircling the right half poles.  The complex values should be plotted on the real and imaginary axes, then we should count the number of contour-clockwise encirclements.  Therefore, if the number of contour-clockwise encirclements equals the number of poles the system is stable.

EE3133-01				EXAM #3			PAGE 3 OF 7

1a con’t)

Standard Nyquist Plot	Plot after Nyquist Criterion is performed.

From the above plots we can see that there is a pole in the R.H.P of the open-loop transfer function thus the system has a closed loop pole in the R.H.P., therefore, p=1. Thus any value of “n” not equal to-1, the system is unstable.

At the end of this problem one can see the plots that were taken using MATLAB software.  From the first plot we can see that their is an encirlcement in the right half plane.  This can be seen in Figure 1.  In order for the system to be stable we need to have it in the left half plane encircling -1 contour-clockwise.  For the following plots there were gains added in order to make the system stable.  The gains were of a negative value.  These can be seen in Figures 2-5.

Use Nyquist criterion, and the gain/phase margin, to determine for what range of values of c the system is stable.

The plots that are labeled with the negative gains show when the system became stable (Figures 2-5).  From the plots one can see that a value of c<0 makes the system become stable.

The gain margin is defined as the change in open loop gain required to make the system unstable.  Systems with greater gain margins can withstand greater changes in system parameters before becoming unstable in closed loop.  The phase margin is defined as the change in open loop phase shift required to make a closed-loop unstable.  It also measures the systems tolerance to time delay.  If there is a time delay greater than 1800 in the loop, the system will become unstable in closed loop.  The time delay can be thought of as a block with a magnitude of 1.

EE3133-01				EXAM #3			PAGE 4 OF 7

1 con’t)

c)  Verify your answer to part (b) using any other technique described in this class.

To verify the system is unstable a Routh-Herwitz was performed.

s1  	-.25c			Because of the sign change is the system is unstable.

s0	1

In order to see what values of c need to be in order for the system to be stable a simple derivation occurs:

Plugging in negative values of c resulted in the system becoming stable.

PROBLEM NO. 2:  In the following circuit, all resistance, capacitance, and inductance values have a magnitude of 1.

Define a set of state variables and justify your answer.

Since there are three different memory elements, there will be three state variables.  These three state variables are the following:

Vc, IL1, IL2

EE3133-01				EXAM #3			PAGE 5 OF 7

2 con’t)

Construct the state equations for this system.

Vc						IL1

CVc = -IR4 + IR5				L1IL1 = -VR4 + Vc + VR6

IR4 = IL1					   VR4 = IL1R4

IR5 = IL2					   VR6 = IL2R7 - Vc

CVc = IL2 - IL2

Therefore,  Vc = IL2/C - IL1/C		Therefore, IL1 = -IL1/L1 + I2/L2

IL2

L2IL2 = VR7 - Vc - VR5

VR5 = IL2R5

VR7 = IL1R6 + Vc

Therefore, IL2 = IL1/L2 - IL2/L2

Output Equations:

Y1 = IL1R4

Y2 = IL2R5

Find the system transfer function (remember this is a matrix).

IL1		  -1	0	 1	  IL1

IL2	    = 	   1	0	-1	  IL2

VC		  -1	0	 1	  Vc

Y1		  1	 0	 0	  IL1

Y2	   =	  0	-1	 0	  IL2

Vc

EE3133-01				EXAM #3			PAGE 6 OF 7

PROBLEM NO. 3:  For the signal x(t) = [sin(2000(t) + cos(3300(t)]u(n),

What is the minimum sample frequency for which this signal can be sampled without loss of information?  Justify your answer.

For the signal to be bandlimited:

fs > 2fh Hz   where fh is the highest frequency.

Therefore, the minimum sampling frequency is 2fh.

Therefore, the minimum sampling frequency is 2(1650)

which equals to 3300 Hz.

Explain how to reconstruct the original signal from the sampled signal.  Be as specific as possible.

The original signal can be reconstructed by passing the sampled signal through a low pass filter.  The cutoff frequencies of the filter are:

Hs(f) = {1/fs, |f| < ½ fs

Therefore the student would select a lowpass filter with a bandwidth of    ½fs and an amplitude response of T.  The output will have a spectrum like the original signal.

Suppose we sample the signal with an 8-bit linear quantizer.  What is the signal to noise ratio of the A/D converter?

SNRdB = # of bits(6dB)

= 8(6dB)

= 48 dB

Derive the Z-transform of x(t) using the following transform:

Z[anu(n)] = 1/1 - az-1

x(t) = [sin(2000(t) + cos(3300(t)]

From Euler’s Theorem

e+ ju = cos u + j sin u

cos u = ½ eju + e-ju

sin u= (eju - e-ju)/2j

EE3133-01				EXAM #3			PAGE 7 OF 7

3d con’t)

# Text boxes

0.25

0.5

y(t)

+

x(t)

c

d/dt

Y(s)

.25

,5X(s) + csY(s)

.5X(s)

X(s)

csY(s)

.5Y(s)

s

+

+

u1(t)

u2(t)

y2(t)

y1(t)

+

-

+