## Slide 1
Objectives: Eigenfunctions Fourier Series of CT Signals Trigonometric Fourier Series Dirichlet Conditions Gibbs Phenomena
Resources: Wiki: Fourier Series Wiki: Eigenfunctions OW: S&S (pp. 177-201) MIT 6.003: Lecture 5 Wolfram: Fourier Series Falstad: Java Applet
• URL: .../publications/courses/ece_3163/lectures/current/lecture_08.ppt
• MP3: .../publications/courses/ece_3163/lectures/current/lecture_08.mp3
LECTURE 08: FOURIER SERIES
Notes: MS Equation 3.0 was used with settings of: 18, 12, 8, 18, 12.

## Slide 2
Representation of CT Signals (Again!)
What is an example of a function when applied to an LTI system produces an output that is a scaled version of itself?
The scale factor, k, is referred to as an eigenvalue. The function, k, is referred to as an eigenfunction.
Using the superposition property of LTI systems:
This reduces the problem of finding the response of any LTI system to any signal to the problem of finding the {k}.
What types of things influence the values {k}? We will soon see that the frequency response of this LTI system is one thing that will influence the shape of the output.
We will later generalize this concept of eigenvalues and eigenfunctions to many types of engineering systems and analyses.
The Fourier series is one of many ways to decompose a signal.
CT LTI
CT LTI

## Slide 3
Eigenfunctions and LTI Systems

## Slide 4
Response of a CT LTI System
Complex exponentials are always eigenfunctions for an LTI system and extremely useful because the output is a scaled version of the input:

## Slide 5
(Complex) Fourier Series Representations
What types of signals can be represented as sums of complex exponentials?
CT: s = j (Fourier Transform)  signals of the form ejt
DT: z = ej (z-Transform)  signals of the form ejn
These representations form the basis of the Fourier Series and Transform.
Consider a periodic signal:
Consider representing a signal as a sum of these exponentials:
Notes:
Periodic with period T
{ck} are the (complex) Fourier series coefficients
k = 0 corresponds to the DC value; k = 1 is the first harmonic; …

## Slide 6
Alternate Fourier Series Representations
For real, periodic signals:
These are essentially interchangeable representations. For example, note:
The complex Fourier series is used for most engineering analyses.
How do we compute the Fourier series coefficients?
There are several ways to arrive at the equations for estimating the coefficients. Most are based on concepts of orthogonal functions and vector space projections.

## Slide 7
Vector Space Projections
How can we compute the Fourier series coefficients?
One approach is to use the concept of a vector projection:
How do we find the components:
We project the vector onto the corresponding axis using a dot product.
Note that this works because the three axes are orthogonal:
We can apply the same concept to signals using the notion of a Hilbert space in which each axis represents an eigenfunction (e.g., cos() and sin()):

## Slide 8
Computation of the Coefficients
We can make use of the principle of orthogonality in the Hilbert space:
(This can be thought of as an “inner product.”)
We can apply this to our Fourier series:
Using the inner product:
This gives us our Fourier series pair (0=2/T):
(synthesis)
(analysis)

## Slide 9
Example: Periodic Pulse Train

## Slide 10
Convergence of the Fourier Series
How can a series composed of continuous functions (e.g., sines and cosines) approximate a discontinuous function, such as a square wave?
Conditions for which the error in this approximation will tend to zero:
X(t) is absolutely integrable over one period:
In a finite time interval, x(t) has a finite number of maxima and minima.
In a finite time interval, x(t) has a finite number of discontinuities.
These are known as the Dirichlet conditions. They will be satisfied for most signals we encounter in the real world. This implies:

## Slide 11
Gibbs Phenomena
Convergence in error can have some interesting characteristics:
This is known as Gibbs phenomena and was first observed by Albert Michelson in 1898.
The Fourier series of a square wave is plotted as a function of N, the number of terms in the finite series.
The limit as N is the average value of x(t) at the discontinuity.
The squared error does converge:

## Slide 12
Introduced the concept of eigenvalues and eigenfunctions.
Developed the concept of a Fourier series.
Discussed three representations of the Fourier series.
Derived an expression for the estimation of the coefficients.
Derived the Fourier series of a periodic pulse train.
Introduced the Dirichlet conditions and Gibbs phenomena.
Discussed convergence properties.
Summary

## Slide 13
Assume we apply a sinewave input to a voltage amplifier under two conditions:
Linear:
In this case, the output is:
The output is a scaled version of the input.
Nonlinear:
Hence, the output signal is at a frequency twice that of the input, which clearly makes this a nonlinear system.
In practice, amplifiers, such as audio power amplifiers, are characterized using a power series:
A single sinewave input generates many frequencies, all harmonically related to the input frequency. This distortion is characterized by figures of merit such as total harmonic distortion and intermodulation. See audio system measurements for more information.
Appendix: Nonlinear Amplifier
Voltage
Amplifier
vin
vout