## Slide 1
Objectives: Generalized Fourier Transform Analog Modulation Amplitude Modulation Angle Modulation Demodulation and Demultiplexing
Resources: Wiki: The Fourier Transform Celier: Generalized Fourier Transform MIT 6.003: Lecture 15 Wiki: Amplitude Modulation RE: AM Demodulation Wiki: Electromagnetic Spectrum Wiki: 700 MHz Auction
• URL: .../publications/courses/ece_3163/lectures/current/lecture_12.ppt
• MP3: .../publications/courses/ece_3163/lectures/current/lecture_12.mp3
LECTURE 12: SIGNAL MODULATION AND DEMODULATION
Notes: MS Equation 3.0 was used with settings of: 18, 12, 8, 18, 12.

## Slide 2
Consider a DC or constant signal:
Compute its Fourier Transform:
Unfortunately, the limit is not finite, and the integral does not converge.
Consider an alternate approach based on an impulse function:
Apply the duality property:
This is known as the Generalized Fourier transform. It allows us to extend the Fourier transform to some additional useful signals such as periodic signals:
The Fourier transform of a periodic signal is a train of impulse functions (and is a line spectrum).
Generalized Fourier Transform

## Slide 3
The electromagnetic spectrum is the most expensive “real estate” in the world. Hence, we would like to make as efficient use of it as possible (e.g., time and frequency domain multiplexing).
It is more efficient (e.g., less power for a given SNR) to transmit signals at higher frequencies.
Modulation: send multiple signals through the same medium (e.g. air, cables, fibers) by simply shifting them to different places in the spectrum.
Amplitude Modulation: carry the information in the amplitude of the signal; use a sinusoidal carrier, c(t).
Angle Modulation: alternate approach in which the signal is carried in the frequency or phase of the carrier signal (frequency and phase modulation).
Many other forms of modulation including pulse-amplitude modulation (PAM), pulse-width modulation (PWM), code division multiple access (CDMA) and spread spectrum. These techniques are typically studied in an introductory course in communications theory.
The Concept of Modulation

## Slide 4
Modulation:
Amplitude Modulation Using a Complex Exponential
Demodulation:
Notes: ]i=k,

## Slide 5
Amplitude Modulation Using a Sinusoid
Notes: ]i=k,

## Slide 6
Synchronous Demodulation of Sinusoidal AM
Assumptions:
 = 0 (for now),
Local oscillator is synchronized with the carrier.
In practice, synchronization is achieved using a phase-locked loop (PLL).
Notes: ]i=k,

## Slide 7
We can easily derive the properties of the demodulated signal:
The low-pass filter removes the high-frequency replica of x(t), leaving only the “baseband” component.
Suppose there is a phase difference between the transmitter and the receiver:
The mismatch in phase appears as a scale factor that can be ignored.
If there is a time-varying phase difference (due to drift):
If the phase difference varies slowly in time, the net result is simply a time-varying amplitude change, which distorts the signal (slightly).
What happens if the receiver is exactly 90 out of phase?
Synchronous Demodulation in the Time Domain
Notes: ]i=k,

## Slide 8
Consider the spectrum of our modulation signal:
Asynchronous Demodulation
Problems if the transmitter and receiver are exactly 90 out of phase.
Alternative: Asynchronous modulation includes the carrier in the output and ensures the envelope of the modulated carrier contains the information.
The carrier must be much higher in frequency than the signal:
Notes: ]i=k,

## Slide 9
Implementation of an Asynchronous Demodulator
AM modulation was popular because of the ease with which it could be demodulated:
However, for this to work, the envelope function must be positive (A+x(t) > 0).
We pay a price in efficiency: more power must be used to guarantee this condition is true.
Notes: ]i=k,

## Slide 10
Double-Sideband Vs. Single-Sideband Modulation
Since x(t) and y(t) are real, from conjugate symmetry, both lower sideband (LSB) and upper sideband (USB) signals carry exactly the same information.
Double-sideband (DSB) occupies 2M bandwidth in  > 0, even though all the information is contained in M.
Single-sideband (SSB) occupies M bandwidth in  > 0.
Of course, SSB requires slightly more complicated hardware, so it was originally only used in applications where bandwidth was very limited (e.g., transcontinental telephone lines).
Analog television signals, which are being obsoleted in February 2009, use a variant of SSB.
Notes: ]i=k,

## Slide 11
Single-Sideband Modulation
Notes: ]i=k,

## Slide 12
Frequency Division Multiplexing
Used in many communications systems including broadcast radio and cell phones.
Notes: ]i=k,

## Slide 13
Summary
Introduced the Generalized Fourier transform.
Demonstrated its use on periodic signals (e.g., Fourier series).
Introduced the concept of modulation.
Discussed amplitude and angle modulation.
Discussed modulation and demodulation of AM signals.
Introduced both a synchronous and asynchronous approach to demodulation.
Introduced techniques used in a variety of common communications systems including single-sideband and double-sideband modulation, and frequency division multiplexing.