## Slide 1
Question: How do you determine the mean time between failures for your “product”?
Objectives: Life Testing Accelerated Life Testing Statistical Models
Resources: Weibull: ALTA NIST: Life Testing
LECTURE 10: ACCELERATED LIFE TESTING
URL:
Notes: MS Equation 3.0 was used with settings of: 18, 12, 8, 18, 12.

## Slide 2
Let’s Start With The Basics…

## Slide 3
What is Accelerated Life Testing?
Traditional life data analysis involves analyzing times-to-failure data (of a product, system or component) obtained under normal operating conditions in order to quantify the life characteristics of the product, system or component.
In many situations, and for many reasons, such life data (or times-to-failure data) is very difficult, if not impossible, to obtain.
Accelerated life testing involves acceleration of failures with the single purpose of quantification of the life characteristics of the product at normal use conditions.
More specifically, accelerated life testing can be divided into two areas: qualitative accelerated testing and quantitative accelerated life testing.

## Slide 4
Qualitative Accelerated Life Testing
Qualitative tests are tests that yield failure information (or failure modes) only.
Common names:
elephant tests
torture tests
Highly Accelerated Life Tests (HALT)
shake and bake tests
Qualitative tests are performed on small samples with the specimens subjected to a single severe level of stress, to a number of stresses or to a time-varying stress.
Qualitative tests are used primarily to reveal probable failure modes.

## Slide 5
Qualitative Accelerated Life Testing (cont.)
Qualitative tests are not designed to yield life data that can be used in subsequent quantitative accelerated life data analysis.
They do provide valuable information as to the types and level of stresses one may wish to employ during a subsequent quantitative test.
Benefits and Drawbacks of Qualitative Tests:
Benefit: Increase reliability by revealing probable failure modes.
Benefit: Provide valuable feedback in designing quantitative tests and in may cases they are a precursor to a quantitative test.
Drawback: What is the reliability of the product at normal use conditions?

## Slide 6
Quantitative Accelerated Life Testing
Designed to quantify the life characteristics of the product, component or system under normal use conditions and thereby provide reliability information.
Reliability information can include the determination of the probability of failure of the product under use conditions, mean life under use conditions and projected returns and warranty costs.
It can also be used to assist in the performance of risk assessments, design comparisons, etc.
Quantitative accelerated life testing can take the form of usage rate acceleration or overstress acceleration.

## Slide 7
Quantitative Accelerated Life Testing (cont.)
For all life tests, some time-to-failure information (or time-to-an-event) for the product is required. Why?
Two methods of acceleration, usage rate acceleration and overstress acceleration, have been devised to obtain times-to-failure data at an accelerated pace.

## Slide 8
Details

## Slide 9
Summary
Many of your projects make claims about reliability, durability, low maintenance, etc.
You must demonstrate how your design has been developed to address these constraints.
Over-engineering is not an acceptable solution.
This is an excellent resource:
http://www.weibull.com/acceltestwebcontents.htm