## Slide 1: Establishing shared features in electroencephalograms
PhD Preliminary Exam
Temple University
College of Engineering
Department of Electrical Engineering
Christian Ward
3 Dec 2015

## Slide 2: Outline
Background
  Motivation for EEG Research
  EEG testing methods
Literature Review
  Makeig
  Peng
  Wulsin
Field of Interest
Applications

## Slide 3: Background
Motivation for this field of research
Current applications and tools

## Slide 4: Motivation
Clinical Diagnosis
Functional Restoration
Stimulus Feedback
Biometric Security
TopLeft – MIT Technology Review. Paralyzed Man’s Arm Wired to Receive Brain Signals. 2015. http://www.technologyreview.com/news/542581/paralyzed-mans-arm-wired-to-receive-brain-signals/
BottomLeft – Peter Brunner et al. Rapid communication with a “P300” matrix speller using electrocorticographic signals (ECoG).” Neuroscience. 2011.

## Slide 5: Applications
Detection of external and internal stimulus responses
  P300, drug studies, behavioral studies, diagnostics
Control of external devices, feedback
  Video games, muscle innervation, prosthesis and augmentation
Brain mapping of physical network
  EEG, fMRI, and MEG
Prediction of shifts in brain state
  Alertness, disease triggers, loss of function
Notes: Be careful of mapping, easy to get tangential to direction of research

## Slide 6: Testing Methods
EEG electrode mappings
  10-20 system, pictured
  Intracranial EEGs
Filtering techniques
  Spatial filtering, known brain structures
  Artifact removal – eye blinks, muscle contractions
Stimulus Triggers
  Evoked Response Potentials (ERPs)
  Medication or simulated stressors
  Objective movement tasks
University of San Diego. BCI2000 Wikipedia. 2015. http://www.bci2000.org/wiki/index.php/User_Tutorial:EEG_Measurement_Setup.
Notes: Control, quantify and time sync from stimulus triggers is difficult

## Slide 7: Literature Review
Scott Makeig et al. Mining Event-Related Brain Dynamics
Hanchuan Peng et al. Feature Selection Based on Mutual Information: Criteria of Max-Dependency, Max-Relevance, and Min-Redundancy
D F Wulsin et al. Modeling electroenchephalography waveforms with semi-supervised deep belief nets: fast classification and anomaly measurement

## Slide 8: Mining Brain Dynamics
Using surface EEG activity to resolve physical location of brain activity and categorizing the associated stimulus response.
Scott Makeig, et al. Mining Event-Related Brain Dynamics. TRENDS in Cog. Neuro. 2004.
Notes: Makeig et al designed an inverse method in which surface EEG activity was used to infer the physical location of activations in the brain. Whereas other investigators focused on averaged ERPs, Makeig et al focused on individual responses to categorize brain activation.

## Slide 9: Event-related Potentials (ERPs)
Triggered in response to auditory or visual stimulus in all subjects with relatively consistent temporal resolution within a subject
University of Waterloo. Event Related Potential Lab. 2015.
https://uwaterloo.ca/event-related-potential-lab/about-event-related-potential-lab/our-research
Notes: Notice timeline on eample. 0 to 600ms, Makeig’s work -500ms to 1500ms! Full dynamic response over time

## Slide 10: Event-related Spectral Perturbations (ERSPs)
Energy changes over the course of the temporal event across the frequency spectrum capture the dynamic environment of the brain
Scott Makeig et al. “Dynamic brain sources of visual evoked responses”. Science. 2002

## Slide 11: Inter-trial Coherence (ITC)
Changes in the phase are unnoticed in the frequency energy levels, but signify a temporal component of the stimulus response.
Scott Makeig et al. “Dynamic brain sources of visual evoked responses”. Science. 2002

## Slide 12: Data
Source EEG is 71 channels
  69 for data following 10-20 layout
  2 for ground/reference
ERSP and ITC
  Calculated at specific electrodes of interest, determined from ICA results
ERP
  Not time average over all stimuli responses
Scott Makeig, et al. Mining Event-Related Brain Dynamics. TRENDS in Cog. Neuro. 2004.

## Slide 13: Independent Component Analysis (ICA)
ICA with Infomax specially made by the group called runica
Spatial filtering and data reduction leading to location mapping on the scalp
Results of ICA return 20 maximally independent components whose scalp maps resemble a dipole projection
Nader Karamzadeh. “Capturing dynamic patterns of task-based functional connectivity with EEG.” NeuroImage. 2013.
Notes: Infomax – attempts to maximize the mutual information between the input values I and the output values O via learning. Typically used by maximizing entropy in ICA, so the inverse ensuring that entropy is high (randomness is at a max) making the two minimally dependent on each other and thus maximally independent

## Slide 14: State space of event related dynamics
Categories of responses:
  ERPs
  Event-related desynchronizations (ERDs)
  Event-related synchronizations (ERSs)
  Partial phase-resetting (PPR)
  “?” as of yet, an unlabeled feature
Scott Makeig, et al. Mining Event-Related Brain Dynamics. TRENDS in Cog. Neuro. 2004.

## Slide 15: Conclusion
Improvements in cognitive neuroimaging and neuroscience now that brain dynamics can be categorized and mapped on a trial by trial basis
Potential to “index brain pathophysiology more accurately than conventional measures” and “may bring non-invasive and invasive electrophysiological research into [a] more direct relationship”.

## Slide 16: Feature Selection Based on Mutual Information
Introduction of the minimal-redundancy-maximal-relevance (mRMR) criterion as a feature selector and comparison against peers
Hanchuan Peng et al. Feature Selection Based on Mutual Information: Criteria of Max-Dependecny, Max-Relevance, and Min-Redundancy. IEEE Trans. Pattern Analysis and Machine Intelligence. 2005
Notes: This paper presents a novel optimization metric for evaluating feature utility.

## Slide 17: Mutual Information
Insight into the activity of one random variable if the state of a different random variable is known
Can be extrapolated to multiple dependencies, but requires some data to build the probability models
Notes: Parzen windows! Discrete to continuous

## Slide 18: Feature Selectors
Maximal Dependency
  To achieve the minimal classification error rate of m features from a given set S(x1 … xm), one needs the maximal statistical dependency of the targeted class (c).
Maximal Relevance
  Select m features from a set (S) with the highest relevance to the target class (c), generally interpreted as features with high mutual information with the target class.
Notes: To minimize the classification error of a set S of m features (x1 .. xm), one needs to maximize the mutual information between the targeted class c and the set S.

## Slide 19: Feature Selectors, cont.
Minimal Redundancy
  Select features with the least overlap among their mutual information, often without aid of the target class
“Minimal-Redundancy-Maximal-Relevance”
  Combination rating of the difference between relevance and redundancy, using redundancy as a penalty

## Slide 20: Filters and Wrappers
Forward Wrapper
  Add features along an optimization parameter
Backward Wrapper
  Remove features along an optimization parameter
Filters do not directly optimize the minimum classification error rate, however they often generate sets that span classifiers robustly
  Ex: mRMR & Max-Relevance

## Slide 21: Classifiers and Data
Classifiers
  Naïve Bayes (NB)
  Support Vector Machines (SVM)
  Linear Discriminant Analysis (LDA)
Testing Method
  10-fold cross validation (10-fold CV)
  Leave One Out Cross Validation (LOOCV)
Continuous Data
  NCI – National Cancer Institute gene data
  LYM – Lymphoma gene features
Discrete Data*
  HDR – handwritten digits
  ARR – Arrhythmia Data
  *made discrete via a Parzen window
Notes: Naïve Bayes – Given x how likely is y if we know the likelihood of x occurring in relation with other random variables
LDA – dot product to

## Slide 22: Data
Hanchuan Peng et al. Feature Selection Based on Mutual Information: Criteria of Max-Dependency, Max-Relevance, and Min-Redundancy. IEEE Trans. Pattern Analysis and Machine Intel. 2005

## Slide 23: Wrapper Effectiveness, Classifier Error
mRMR outperforms other features across nearly all classifiers and data sets, however the performance is not consistent
Hanchuan Peng et al. Feature Selection Based on Mutual Information: Criteria of Max-Dependecny, Max-Relevance, and Min-Redundancy. IEEE Trans. Pattern Analysis and Machine Intelligence. 2005
Notes: Label numbers. Why not in that one case of NCI, LDA, mRMR? NEW SLIDE

## Slide 24: Computational Effectiveness
mRMR’s time to compute features is a considerable improvement on continuous data. Using 40 features exceeds the number of classes in each data set and, in some cases, exceeds the number of training samples.
Hanchuan Peng et al. Feature Selection Based on Mutual Information: Criteria of Max-Dependecny, Max-Relevance, and Min-Redundancy. IEEE Trans. Pattern Analysis and Machine Intelligence. 2005

## Slide 25: Conclusion
Given enough features mRMR always wins out, but with less features the results aren’t clear. The best feature selection does not indicate the best number of features.
Hanchuan Peng et al. Feature Selection Based on Mutual Information: Criteria of Max-Dependecny, Max-Relevance, and Min-Redundancy. IEEE Trans. Pattern Analysis and Machine Intelligence. 2005

## Slide 26: Semi-supervised Deep Belief Nets
Performance of a raw data fed Deep Belief Network for real time feature detection compared to other common techniques
D F Wulsin et al. Modeling electroencephalography waveforms with semi-supervised deep belief nets: fast classification and anomaly measurement. J. Neural Eng.. 2011

## Slide 27: Data Sets and Evaluation
Data Source
  256Hz sample rate from 11 patients
  Separated into channel-seconds pulled randomly from 13 2hr annotated segments
  All data is normalized
raw256
  Uses the original data source
feat16
  KNN (k=3) selected hand-define features
pca20
  Resolves first 20 eigenvectors that account for 92.75% of the variance
Detection performance stems from the F1 measure
Speed is evaluated w.r.t. performance in seconds
Notes: More notes about the data

## Slide 28: Features
D F Wulsin et al. Modeling electroencephalography waveforms with semi-supervised deep belief nets: fast classification and anomaly measurement. J. Neural Eng.. 2011
Background
Spike & Sharp Wave
GPED & Triphasic
PLED
Eye Blink
Notes: GPED – generalized periodic discharge
PLED – periodic lateralized epileptiform discharge

## Slide 29: Classifiers
Decision Trees (DTs)
  Using Gini diversity index where R is the data set and p the probabilities of each item in the set
Support Vector Machines (SVMs)
  Using radial basis function kernel where x and x’ are two samples and σ is a free parameter

## Slide 30: Classifiers, cont.
K-Nearest Neighbor (KNN)
  Nonparametric clustering based upon
Deep Belief Networks (DBNs)
  Layered neural network useful in supervised and unsupervised learning
LEFT: Burton DeWilde. Classification of Hand-written Digits. 2012. http://bdewilde.github.io/blog/blogger/2012/10/26/classification-of-hand-written-digits-3/
RIGHT: D F Wulsin et al. Modeling electroencephalography waveforms with semi-supervised deep belief nets: fast classification and anomaly measurement. J. Neural Eng.. 2011

## Slide 31: Boltzmann Machines
Network of units providing ‘energy’ related to their state with respect to each node’s bias, a for visible and b for hidden, and their connectivity weights w
Notes: Less it more! Find sort discription

## Slide 32: Deployment of DBN via Layers
G.E. Hinton et al. Reducing the Dimensionality of Data with Neural Networks. 2006

## Slide 33: Results, classification
Classification amongst all approaches appears comparable, slightly worse for PCA data
D F Wulsin et al. Modeling electroencephalography waveforms with semi-supervised deep belief nets: fast classification and anomaly measurement. J. Neural Eng.. 2011
Notes: Are these results anticipated? Why do certain data sets struggle, why do specific classifiers struggle?

## Slide 34: Results, speed
DBN consistently ranks second in speed behind DTs while SVM keeps out using modified data
D F Wulsin et al. Modeling electroencephalography waveforms with semi-supervised deep belief nets: fast classification and anomaly measurement. J. Neural Eng.. 2011
Notes: Is faster better?

## Slide 35: Conclusion
DBNs can operate faster with equal effectiveness as other implementations to provide real-time monitoring
D F Wulsin et al. Modeling electroencephalography waveforms with semi-supervised deep belief nets: fast classification and anomaly measurement. J. Neural Eng.. 2011

## Slide 36: Research Questions

## Slide 37: Questions
Is it possible to find universal features that span individuals? Stimuli? Brain states?
Do biological constraints lead to better features or do unsupervised approaches remove inherent bias?
Can EEG data be separated into partitions pertaining to subject identity, subject condition, and subject activity?
Features versus classifier, which drives success more effectively?
How could a DBN be designed to ‘learn’ without full retraining? Augmenting the learned layers as new data becomes available?

## Slide 38: Applications

## Slide 39: Potential Applications
Leverage the speed and effectiveness of DBNs to search large databases for ‘similar’ features given a sample signal
  Would need an open data set to ‘learn’ how to evaluate not for features, but for qualities of those features
  Can previously built layers be updated as more data becomes available to mitigate full re-training
Separate data into individual, intent, and response to understand the space each occupies in signal
  Makeig found a way to resolve ERP data into a direct mapping of location, complete with characterization of stimulus response
  Peng showed it is difficult to evaluate features alone, but is there a way to link annotated features or biology with the analysis to address redundancy in EEG data

## Slide 40: Thanks
Questions?

## Slide 41: Backward and Forward Selection Error
Attempts to ensure addition or removal of features does not make the classification error any worse during the search process. Ideally the chosen feature leads to the largest reduction in classification error.
However, it is often not possible to reduce, or increment, the feature set without adding more error. Additionally, there may be a need to reach a certain number of features regardless of the error changes or necessary to compare two sets against each other.
Given two sets, S1 and S2, of n features comparing classification error does not provide the fullest insight into the better feature set. More often the set that is recursively more characteristic, where its subsets of feature groups perform better, e1 < e2, over the range of n features. A rating, ρ, is used to indicate how many subsets pass this criteria suggesting which full set is RM-characteristic.

## Slide 42: Max Dependency, more detail
The addition of the mth feature depends on finding the largest increase in given the present feature set

## Slide 43: Optimal First-Order Incremental Selection
Theorem: For the first-order incremental search, mRMR is equivalent to Max-Dependency. If mRMR cannot match the classification accuracy statistically it really can’t be used!
for scalar variables
for scalar variables
Notes: H is entropy of the variables

## Slide 44: Optimal First-Order Incremental Selection
Notes: 1. Minimizing JðSmÞ only is equivalent to searching mutually exclusive (independent) features.2 This is
insufficient for selecting highly discriminative features.
2. Maximizing JðSm; cÞ only leads to Max-Relevance. Clearly, the difference between mRMR and Max- Relevance is rooted in the different definitions of dependency (in terms of mutual information). Equation (10) does not consider the joint effect of features on the target class. Onthe contrary, Max-Dependency((2) and (3)) considers the dependency between the data distribution in subspace Rm and the target class c. This difference is critical in many circumstances.
3. The equivalence between Max-Dependency and mRMR indicates mRMR is an optimal first-order implementation scheme of Max-Dependency.
4. Compared to Max-Dependency, mRMR avoids the estimation of multivariate densities pðx1; . . . ; xmÞ
and pðx1; . . . ; xm; cÞ. Instead, calculating the bivariate density pðxi; xjÞ and pðxi; cÞ could be much easier
and more accurate. This also leads to a more efficient feature selection algorithm.

## Slide 45: Parzen Window
Given N samples of a variable x, the approximate density function p̂(x) has the following form:
Where δ(.) is the Parzan function, h is the window width, Σ is the covariance of z, and d is the dimension of x.

## Slide 46: Wrapper Effectiveness, Error Change
Data Set | Wrapper | NB |  | SVM |  | LDA | 
 |  | MaxRel - mRMR | mRMR, FWD-BKW | MaxRel - mRMR | mRMR, FWD-BKW | MaxRel - mRMR | mRMR, FWD-BKW
HDR | Forward | 3.25 | 0.10 | 2.05 | 0.60 | 2.75 | 0.05
 | Backward | 2.85 |  | 1.70 |  | 2.90 | 
ARR | Forward | 0.95 | 0.00 | 1.66 | -0.30 | 1.66 | -0.23
 | Backward | 5.24 |  | 0.89 |  | 2.15 | 
NCI | Forward | 13.34 | -1.67 | 3.33 | 8.34 | -1.66 | 8.33
 | Backward | 5.00 |  | 5.00 |  | 5.00 | 
LYM | Forward | 1.04 | 2.08 | 4.17 | -1.05 | 4.17 | -1.05
 | Backward | 2.08 |  | 0.00 |  | 3.12 | 
NCI – 9703 variables, 60 samples, 9 classes where 1/60 = 1.6667%

## Slide 47: Wrapper Effectiveness, Missed Samples
Data Set | Wrapper | NB |  | SVM |  | LDA | 
 |  | MaxRel | mRMR | MaxRel | mRMR | MaxRel | mRMR
HDR | Forward | 129.00 | 64.00 | 110.00 | 69.00 | 136.00 | 81.00
 | Backward | 119.00 | 62.00 | 91.00 | 57.00 | 138.00 | 80.00
ARR | Forward | 79.00 | 75.01 | 87.99 | 81.02 | 82.99 | 76.02
 | Backward | 97.02 | 75.01 | 86.02 | 82.28 | 86.02 | 76.99
NCI | Forward | 16.00 | 8.00 | 15.00 | 13.00 | 19.00 | 20.00
 | Backward | 12.00 | 9.00 | 11.00 | 8.00 | 18.00 | 15.00
LYM | Forward | 6.00 | 5.00 | 6.00 | 2.00 | 6.00 | 2.00
 | Backward | 5.00 | 3.01 | 3.01 | 3.01 | 6.00 | 3.01
1/2000 = 0.05% 1/420 = 0.23809% 1/60 = 1.6667% 1/96 = 1.041%

## Slide 48: Wulsin Data Details

## Slide 49: Classifier Search Parameters

## Slide 50: DBM & RBM details
Probability of a given set of visible and hidden states weighted according to all possible pairs of states.
The probability of the two given states, data versus model, drive the updates of the weights connecting them. The learning rate must be specified by the user.

## Slide 51: RBM learning
Generating unbiased data is easy in that it requires a random visible or hidden layer, to make the corresponding.
Generating unbiased data from the model is difficult since it requires the model to be agitated to produce a resultant visible or hidden state that matches the given configuration.

## Slide 52: Are the raw256 and feat16 data sets unique enough?
Via the Wilcoxan-Mann-Whitney test, the null hypothesis that the differences between the median RMSE values of background and non-background datasets are not significant can be rejected.

## Slide 53: Why are Wulsin’s F1 scores so poor?
Closed data set, 11 subjects
  Using only a very small portion of all recorded data
    Randomly subsampled one thousand 2 minute segments across all channels from 13 2hr blocks where activity was prevalent
    The annotations comes from 50 random 2 min segments annotated over all channels
The Appraiser Bias Problem
  “Human labeling of specific waveforms is itself a very difficult task, and the inter-rater reliability among board certified neurophysiologists is usually low [18, 21, 22]. For computational simplicity, we constrained our classifiers to only examine individual channel-seconds, when in reality experts incorporate much greater spatial and temporal information in their markings. These factors kept our expectations modest for the ultimate recall and precision of our classifiers.”