## Slide 1: Strategies for Sparsity-based Time-Frequency Analyses
Shuimei Zhang
Department of Electrical and Computer Engineering
Temple University, Philadelphia, USA
http://asplab.net
Advanced
Signal
Processing
Laboratory

## Slide 2: Outline
Introduction
Signal Model
Atomic Norm-based TFR Reconstruction
AAO-based TFR Reconstruction
Future Work: Radar Waveform Recognition

## Slide 3: Introduction
Most real-world signals are nonstationary in nature such as electroencephalogram (EEG), music, radar.
EEG1
Music2
Radar3
1 https://www.biofeedback-tech.com/articles/2016/5/26/eeg-fourier
2 https://atmos.uw.edu/~breth/classes/AS552/matlab/lect/html/music.html
3 https://www.mathworks.com/help/phased/examples/signal-parameter-estimations-in-a-radar-warning-receiver.html

## Slide 4: Introduction
Nonstationary random process: violate any of the properties that define a wide-sense stationary process (WSS)1
Nonstationarity relates to the variation over time of the statistics of the signal.
Time domain
Frequency domain
Time-Frequency domain
Linear frequency modulated signal
WSS: mean and auto-correlation function do not depend on the absolute time

## Slide 5: Introduction
Google Soli: https://atap.google.com/soli/technology/
Q. Wu, Y. D. Zhang, W. Tao, and M. G. Amin, “Radar-based fall detection based on Doppler time-frequency signatures for assisted living,” IET Radar, Sonar & Navigation, special issue on Application of Radar to Remote Patient Monitoring and Eldercare, vol. 9, no. 2, pp. 164-172, Feb. 2015.

## Slide 6: Introduction
Nonstationary signal
time-frequency representation (TFR)
Linear
Short-time Fourier transform (STFT)
Wavelet transform
Bilinear
Wigner-Ville distribution
Time-frequency kernel and Cohen’s class

## Slide 7: Signal Model
Consider a discrete-time -component frequency modulated (FM) signal
Instantaneous frequency (IF) of the th component
In practice, signal is corrupted by noise
amplitude
phase law

## Slide 8: Signal Model
Instantaneous autocorrelation function (IAF):
Wigner-Ville distribution (WVD):
Ambiguity function (AF):

## Slide 9: Signal Model
FFT (q, t)
Waveform (real part)
IAF
Ambiguity function
Cross-terms
Auto-terms
Time-frequency distribution
Cross-terms
Auto-terms
2-D FFT
FFT (f, t )
WVD provides high time-frequency (TF) concentration for linear FM signals.
Cross-terms are unavoidable due to bilinear nature in the cases of nonlinear or multiple components.
Cross-terms appear in the middle-way of auto-terms in the TF domain.

## Slide 10: Signal Model
Auto-terms are located around the origin of the ambiguity domain, and cross-terms tend to be away from the origin.
Time-frequency kernel is a low-pass filter in the ambiguity domain.
  Data-independent: e.g., Choi-Williams distribution (CWD)
  Data-dependent: e.g., adaptive optimal kernel (AOK)
CWD
AOK

## Slide 11: Signal Model
In practice, missing samples frequently occur.
Examples:
Light-of-sight obstruction
Multipath fading
Removal of impulsive noise or jammer
Burst missing samples!
(Missing samples appear as clusters)

## Slide 12: Effects of Missing Samples
No
Missing
Random
Missing
IAF
AF
WVD
AOK
Burst
Missing

## Slide 13: Effects of Amplitude Difference
IAF
AF
WVD
AOK
No
Missing
Burst
Missing
Another challenge is the amplitude difference of the signal components. It is diﬃcult to identify the auto-term associated with the weak signal component from the residual artifacts of the cross-terms.

## Slide 14: Proposed Methods
IAF Interpolation
Recover Burst Missing Samples
Suppress Cross-Terms
High-Resolution TFR
Time-Frequency Kernel
Sparse Reconstruction
Robust TFR in Impaired Observing Environments
eg: burst missing samples, noisy environments, amplitude difference
Atomic Norm-based TFR Reconstruction Method
AAO-based TFR Reconstruction Method
Application: radar waveform recognition

## Slide 15: Atomic Norm-based TFR Reconstruction Method
S. Zhang and Y. D. Zhang, "Robust time-frequency analysis of multiple FM signals with burst missing samples," IEEE Signal Processing Letters, vol. 26, no. 8, pp. 1172-1176, Aug. 2019.

## Slide 16: Compressive Sensing
The required number of samples for reconstructing a signal can be greatly reduced if it is sparse in a known discrete basis.

## Slide 17: Basis Mismatch
Compressive sensing
Known discrete dictionary
VS
Real world signal
Sparse in a continuous dictionary
In the presence of basis mismatch ( ), exact or near-exact sparse recovery cannot be guaranteed. Recovery may suffer large errors.
source: Y. Chi, 2014 ICASSP tutorial
Spectrally sparse signal .
Frequency mismatch

## Slide 18: Going Off The Grid
Parameter estimation without discretization with theoretical guarantees.
The atomic norm was first proposed in [1] as a general framework for designing tight convex relaxations to promote simple signal decompositions.
People seeks to use a minimal number of atoms to represent a given signal from an atomic set composed of an ensemble of signal atoms.
Atomic Norm Minimization
Signal Recovery
Covariance Matrix Estimation
[1] V. Chandrasekaran, B. Recht, P. A. Parrilo, A. S. Willsky, “The convex geometry of linear inverse problems,” Foundations of Computational Mathematics 12 (6) (2012) 805–849.

## Slide 19: Atomic Norm
Special cases of the atomic norm
Sparse signals: an atom for sparse signals is a normalized vector of sparsity one, and the atomic norm is norm
Low-rank matrices: an atom for low-rank matrices is a normalized rank-one matrix; and the atomic norm is nuclear norm
The set of atoms is graphed in red. Image credit: Y. Chi, 2014 ICASSP tutorial

## Slide 20: Atomic Norm-based TFR Reconstruction
In general, radar signals exhibit low occupancy in the TF domain, thus casting them as sparse in the joint-variable representations.
Consider non-zero entries in . The IAF is the IDFT of WVD
IAF slice
TF slice
Lag vector:
IDFT
IAF slice
TF slice

## Slide 21: Atomic Norm-based TFR Reconstruction
Construct a Hankel matrix from IAF slice
Step 1: Define an atom for representing as
Atomic set is
Same frequency components are shared among all the columns
Note that is continuous-valued , such that the basis mismatch issue is avoided.

## Slide 22: Atomic Norm-based TFR Reconstruction
Step 2: Define the atomic norm of as
Step 3: Formulate a convex program to minimize the atomic norm
The convex hull of
Vandermonde decomposition lemma: exists
trace operator
: Hermitian Toeplitz matrix with as its first column

## Slide 23: Atomic Norm-based TFR Reconstruction
In the presence of noise,
: noisy IAF slice at time instant (observed) : observation pattern
: clean IAF slice at time instant (to be estimated) noise level

## Slide 24: Atomic Norm-based TFR Reconstruction
Stage 1: IAF Interpolation via atomic norm minimization
Stage 2: cross-term mitigation via kerneled IAF
AOK

## Slide 25: Atomic Norm-based TFR Reconstruction
Stage 3: rank deduction to further reduce the residual artifacts
A rule of thumb for determining the value of is to retain enough singular values to make up around 95% of the energy in
Singular value decomposition
IAF slice from
Only keep first principal singular values from

## Slide 26: Atomic Norm-based TFR Reconstruction
High-resolution TFR via sparse reconstruction
We choose orthogonal matching pursuit (OMP) to solve the sparse reconstruction problem, since it allows us to specify the sparsity at each time instant.
TF slice
IAF slice
IDFT dictionary matrix

## Slide 27: Simulation Setting
Two-component linear FM (LFM) and nonlinear FM (NLFM) with different amplitudes
Unless otherwise specified
T = 128
48 missing samples (4 missing samples each burst, 12 bursts)
No noise considered
Mean square error (MSE) comparison: 50 simulation runs

## Slide 28: Simulation Results: Two-Component LFM
No missing: baseline IAF and WVD
Burst missing
Stage1: IAF interpolation (Atomic norm)
Stage2: cross-term mitigation
(Atomic norm + AOK)

## Slide 29: Simulation Results: Two-Component LFM
Stage3: further improvement
(Atomic norm + AOK + rank deduction)
For comparison
(AOK + OMP)
Proposed TFR
Atomic norm
+
AOK
+
rank deduction
+
OMP
Proposed method perfectly recovered both the two LFM signal components.

## Slide 30: Simulation Results: Two-Component NLFM
No missing: baseline IAF and WVD
Burst missing
Stage1: IAF interpolation (Atomic norm)
Stage2: cross-term mitigation
(Atomic norm + AOK)

## Slide 31: Simulation Results: Two-Component NLFM
Stage3: further improvement
(Atomic norm + AOK + rank deduction)
For comparison
(AOK + OMP)
Proposed TFR
Atomic norm
+
AOK
+
rank deduction
+
OMP
Proposed method provides much more consistent TFR

## Slide 32: Simulation Results: Noisy Environments
TABLE. MSE comparison between the baseline IAF and the IAF obtained with atomic norm-based IAF (AT), and the incomplete data (Miss)
Proposed method consistently reduces the MSE of the reconstructed IAF. Better performance for LFM in high SNRs.

## Slide 33: AAO-based TFR Reconstruction Method
S. Zhang and Y. D. Zhang, “Low-rank Hankel matrix completion for robust time-frequency analysis,” submitted to IEEE Transactions on Signal Processing.

## Slide 34: Issues in Atomic Norm based Method
Requirement: High-sparsity of the signal representations in the time-frequency domain or the ambiguity function domain
High-occupancy cross-terms
eg: Nonparallel FM or NLFM
Invalid high-sparsity assumption

## Slide 35: Issues in Atomic Norm based Method
Two-component LFM
Parallel
At time instant t
is a constant
For IAF slice
If nonparallel, is not a constant anymore for IAF slice
The number of non-zero entries will be much larger than 3.

## Slide 36: Issues in Atomic Norm based Method
Two-component NLFM
where

## Slide 37: Issues in Atomic Norm based Method
If parallel, we will have
High-occupancy cross-terms exists even if the two NLFM are parallel, not to mention nonparallel case

## Slide 38: AAO-based TFR Reconstruction
IAF interpolation
via annihilating ﬁlter based low-rank Hankel matrix (ALOHA)
Cross-term mitigation via AOK
High-resolution TFR reconstruction via OMP
A limited set of FM signals:
atomic norm-based TFR
A general class of FM signals:
AAO-based TFR

## Slide 39: AAO-based TFR Reconstruction
Auto-terms does not drastically vary within a short time window
Cross-terms oscillate with fast phase variation over time
Proper selected IAF patch can lead to a sparse spectrum, i.e., Doppler-frequency (DF) is sparse.
DF obtained from the IAF patch

## Slide 40: AAO-based TFR Reconstruction
The associated spectrum of IAF patch
There exists a corresponding annihilating filter1,2
1 K. H. Jin and J. C. Ye, “Annihilating filter-based low-rank Hankel matrix approach for image inpainting,” IEEE Trans. Image Process., vol. 24, no. 11, pp. 3498–3511, Nov. 2015.
2 J. C. Ye, J. M. Kim, K. H. Jin, and K. Lee, “Compressive sampling using annihilating filter-based low-rank interpolation,” IEEE Trans. Inf. Theory, vol. 63, no. 2, pp. 777–801, Feb. 2016.
Sparsity in the primary space
Low rankness of a structured matrix in the spectral domain
Fundamental duality

## Slide 41: AAO-based TFR Reconstruction
Construct a block Hankel matrix from IAF patch

## Slide 42: AAO-based TFR Reconstruction
Problem formulation
Nuclear norm normalization
: noisy IAF patch (observed) : observation pattern
: clean IAF patch (to be estimated) noise level

## Slide 43: AAO-based TFR Reconstruction
We can reformulate this problem into the augmented Lagrangian form
The problem can be solved in an alternating direction method of multiplier (ADMM)-based technique

## Slide 44: AAO-based TFR Reconstruction
ADMM

## Slide 45: AAO-based TFR Reconstruction
Patch Size Selection Principle
Desired IAF patch size Sparse IAF spectrum (DF domain)
Variation of the IFs should be kept small in the selected patch
Dynamic Range
Frequency Difference

## Slide 46: Simulation Setting
Two-component signal
Unless otherwise specified
T = 128
52 missing samples (4 missing samples each burst, 13 bursts)
No noise considered
Mean square error (MSE) comparison: 50 simulation runs
Patch size: 27 27 with pencil parameters

## Slide 47: Simulation Results: Two Parallel NLFM
No missing: baseline IAF and WVD
Burst missing
Atomic norm-based Method
Proposed AAO Method

## Slide 48: Simulation Results: One Sine and One LFM
No missing: baseline IAF and WVD
Burst missing
Atomic norm-based Method
Proposed AAO Method

## Slide 49
Simulation Results: One Sine and One LFM
TABLE. MSE comparison between the baseline IAF and the IAF obtained with the incomplete data (Miss), atomic norm-based IAF (AT), and the proposed ALOHA-based IAF
The proposed AAO method provides much lower MSE between the baseline IAF and the reconstructed IAF, especially in high SNR cases.

## Slide 50: Future Work: Radar Waveform Recognition
Preliminary results accepted for presentation:
S. Zhang, A. Ahmed, and Y. D. Zhang, “Sparsity-based time-frequency analysis for automatic radar waveform recognition,” IEEE International Radar Conference, Washington DC, April 2020.
.

## Slide 51: Radar Waveform Recognition
Automatic radar waveform recognition plays an important role in electronic warfare, such as radar emitter identiﬁcation and threat detection, especially for low probability of intercept (LPI) radar.
P2 Code
T1 Code
Costas
LFM
Common LPI radar waveforms

## Slide 52: Radar Waveform Recognition
Feature extraction and classifier design are two key procedures for radar waveform recognition.
The noise will introduce the artifacts in the TFR, which prohibits the effective feature extraction.
Provide enhanced TFR
IAF denoising: atomic norm minimization
Cross-term mitigation: CWD
High resolution TFR: sparse reconstruction via OMP
Improved feature extraction

## Slide 53: Signal Denoising via Atomic Norm Minimization
Problem formulation
Hankel matrix obtained from noisy IAF slice (observed)
Hankel matrix obtained from clean IAF slice (to be estimated)

## Slide 54: Simulation Setting
P2 Code signal
Number of phase M: 6
Cycles per phase code: 1
Input signal to noise ratio (SNR): 0 dB

## Slide 55: Simulation Results: P2 Code Signal
Waveform
No
noise
IAF
WVD
CWD
0dB
SNR

## Slide 56: Simulation Results: P2 Code Signal
Denoised IAF
Denoised CWD
Proposed TFR
(Atomic nom + CWD +OMP)
Proposed method not only mitigates the effects of the noise, but also provides a high-resolution TFR, thereby signiﬁcantly improving the feature representation of the radar signals.

## Slide 57: Simulation Results: Waveform Recognition
TABLE. List of the parameters of simulated signals
1000 samples (input SNR = 0dB) for each class
75% for training, 25% for testing

## Slide 58: Simulation Results: Waveform Recognition
TABLE. List of the parameters of the CNN structure

## Slide 59: Simulation Results: Waveform Recognition
CWD-based TFR
Proposed TFR
(Atomic nom + CWD +OMP)
Proposed method helps to improve average classification accuracy from 90.24% to 97.76%

## Slide 60: Future Work
Develop a more general and effective pre-processing algorithm for radar waveform recognition
Explore the ALOHA-based IAF denoising algorithm
Utilize the data independent kernel
Explore other state-of-the-art deep learning techniques such as residual network (ResNet) to further illustrate the effectiveness of the proposed pre-processing algorithms

## Slide 61: Future Work
TABLE. Timeline for future work

## Slide 62: Publications
I have mainly worked on the following projects:
Sparsity based time-frequency analysis
Accepted: 1 Journal Paper, 1 Conference Paper
Under Review: 1 Journal Paper
Under Preparation: 1 Journal Paper
Source localization in a scalable UAV network
Accepted: 3 Conference Paper
Spectrum sharing among radar, communications, and radio astronomy
Accepted: 1 Journal Paper, 5 Conference Papers
Under Review: 1 Journal Paper (Minor Revision)

## Slide 63: Journal Papers
Accepted:
S. Zhang, Y. Gu, and Y. D. Zhang, “Robust astronomical imaging in the presence of radio frequency interference,” Journal of Astronomical Instrumentation, vol. 8, no. 1, pp. 1–15, March 2019.
S. Zhang and Y. D. Zhang, “Robust time-frequency analysis of multiple FM signals with burst missing samples,” IEEE Signal Processing Letters, vol. 26, no. 8, pp. 1172–1176, Aug. 2019.
Under Review
A. Ahmed, S. Zhang, and Y. D. Zhang, “Antenna selection strategy for transmit beamforming-based joint radar-communication system ,” submitted to Digital Signal Processing (Minor Revision)
S. Zhang and Y. D. Zhang, “Low-rank Hankel matrix completion for robust time-frequency analysis,” submitted to IEEE Transactions on Signal Processing

## Slide 64: Conference Papers
S. Zhang, Y. Gu, B. Wang, and Y. D. Zhang, “Robust astronomical imaging under coexistence with wireless communications,” Asilomar Conference on Signals, Systems, and Computers, Paciﬁc Grove, CA, Oct. 2017.
S. Zhang, Y. Gu, W. C. Barott, and Y. D. Zhang, “Improved radio astronomical imaging based on sparse reconstruction,” SPIE Compressive Sensing Conference, Orlando, FL, April 2018.
S. Zhang, Y. Gu, C-H. Wong, and Y. D. Zhang, “Dimension-reduced radio astronomical imaging based on sparse reconstruction,” IEEE Sensor Array and Multichannel Signal Processing Workshop, Sheﬃeld, U.K., July 2018.
S. Zhang, A. Ahmed, and Y. D. Zhang, “Sparsity-based collaborative sensing in a scalable wireless network,” SPIE Compressive Sensing Conference, Baltimore, Maryland, April 2019.
A. Ahmed, S. Zhang, and Y. D. Zhang, “Multi-target motion parameter estimation exploiting collaborative UAV network,” IEEE International Conference on Acoustics, Speech, and Signal Processing, Brighton, U.K., May 2019.

## Slide 65: Conference Papers
S. Zhang, A. Ahmed, and Y. D. Zhang, “Robust source localization exploiting collaborative UAV network,” Asilomar Conference on Signals, Systems, and Computers, Paciﬁc Grove, CA, Nov. 2019.
A. Ahmed, S. Zhang, V. S. Amin, and Y. D. Zhang, “Spectrum sharing strategy for radio frequency-based medical services,” IEEE Signal Processing in Medicine and Biology Symposium, Philadelphia, PA, Dec. 2019.
S. Zhang, A. Ahmed, and Y. D. Zhang, “Sparsity-based time-frequency analysis for automatic radar waveform recognition,” IEEE International Radar Conference, Washington DC, April 2020.
A. Ahmed, S. Zhang, and Y. D. Zhang, “Optimized sensor selection for joint radar-communication systems,” IEEE International Conference on Acoustics, Speech, and Signal Processing, Barcelona, Spain, May 2020.
S. Zhang, A. Ahmed, Y. D. Zhang, and S. Sun, “DOA Estimation Exploiting Interpolated Multi-Frequency Sparse Array,” IEEE Sensor Array and Multi channel Signal Processing Workshop, Hangzhou, China, June 2020.

## Slide 66
http://asplab.net
Advanced
Signal
Processing
Laboratory